## Slide 1: MIET2385 Systems Engineering Principles Systems Engineering V Lifecycle – High Level Design – Functional Analysis – Tutorial – Electrical bicycle
Professor John Mo
Building 251, Level 2, Room 27
Email: john.mo@rmit.edu.au

## Slide 2: Function Re-use, Re-cycle, Re-generate
An important objective of functional analysis is to consider strategically, whether functions in the system can be re-used due to variations in the system design, compatibility, component availability.
Variations in system application are best handled with re-use, re-cycle, re-generate from a template model.

## Slide 3: Electric Bicycle

## Slide 4: Concept of Operations Electric Bicycle
Concept of operations of the system depends on what the user intends to do with the system
Single person travel (urban areas)
Multiple (2) persons (urban areas)
Small goods delivery (urban areas)
Single person travel (long distance)
Small goods delivery (long distance)

## Slide 5: Concept of Operations Type A (Single person urban areas)
Put helmet on.
Release the stand. Hands to hold the handles.
Sit on the bicycle. Feet on ground to support bicycle.
Insert key to bicycle. Turn power on.
Turn right handle forward to increase speed, allow right handle to relax to continue without adding power.
System limits max. speed 20 kmph (urban limit)
If more power is required, activate power surge function, then cycle paddle to assist.
Turn steering column to turn direction.
To stop, turn right handle backward to activate regenerative brake.
Wait to stop then put feet on ground to support bicycle.
Turn power off.
Step out of bicycle.
Put on stand.

## Slide 6: Hierarchy of Functions – Electric Bicycle Type A operation Single person travel (urban areas)
F0 – To travel around town on two wheels (1 rider)
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security

## Slide 7: FFBD Type A (Single person urban areas)
Electric bicycle (Level 0 Function)
Person at starting location
Arrive destination
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
System control activated
Activation authorised
Control manual power
System auto-power
System manual-power
System speed

## Slide 8: Concept of Operations Type B (Multiple – 2 riders)
Put extra seat at back of bicycle.
Both persons put helmets on.
Release the stand. Hands to hold the handles.
Driver sits on the bicycle, puts feet on ground to support bicycle.
Passenger sits on the bicycle.
Driver Inserts key to bicycle. Turn power on.
Turn right handle forward to increase speed, allow right handle to relax to continue without adding power.
System limits max. speed 20 kmph (urban limit)
If more power is required, activate power surge function, then cycle paddle to assist.
Turn steering column to turn direction.
To stop, turn right handle backward to activate regenerative brake.
Wait to stop then put feet on ground to support bicycle.
Turn power off.
Passenger steps out of bicycle.
Driver steps out of bicycle..
Put on stand.

## Slide 9: Hierarchy of Functions – Electric Bicycle Type B operation (Multiple – 2 riders)
F0 – To travel around town on two wheels (2 riders)
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security

## Slide 10: FFBD Type B (Two persons, urban areas)
Electric bicycle (Level 0 Function)
Person at starting location
Arrive destination
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
System control activated
Driver ready to activate system
Control battery power
Control manual power
System auto-power
System manual-power
System speed

## Slide 11: Concept of Operations Type C (Goods, urban area)
Put goods carrier at back of bicycle.
Put helmet on.
Release the stand. Hands to hold the handles.
Sit on the bicycle. Feet on ground to support bicycle.
Insert key to bicycle. Turn power on.
Turn right handle forward to increase speed, allow right handle to relax to continue without adding power.
System limits max. speed 20 kmph (urban limit)
If more power is required, activate power surge function, then cycle paddle to assist.
Turn steering column to turn direction.
To stop, turn right handle backward to activate regenerative brake.
Wait to stop then put feet on ground to support bicycle.
Turn power off.
Step out of bicycle.
Put on stand.
Unload goods from goods carrier.

## Slide 12: Hierarchy of Functions – Electric Bicycle Type C operation (Goods, urban area)
F0 – To travel around town on two wheels (Goods, urban area)
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security

## Slide 13: FFBD Type A (Two persons urban areas)
Electric bicycle (Level 0 Function)
Person at starting location
Arrive destination
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
System control activated
Driver ready to activate system
Control battery power
Control manual power
System auto-power
System manual-power
System speed

## Slide 14: Concept of Operations Type D (Single person, long distance)
Put armed seat with seat belt (to enhance seating).
Put helmet on.
Release the stand. Hands to hold the handles.
Sit on the bicycle. Feet on ground to support bicycle.
Insert key to bicycle. Turn power on.
Turn right handle forward to increase speed, allow right handle to relax to continue without adding power.
System limits max. speed 60 kmph (safety limit)
If more power is required, activate power surge function, then cycle paddle to assist.
Turn steering column to turn direction.
To stop, turn right handle backward to activate regenerative brake.
Wait to stop then put feet on ground to support bicycle.
Turn power off.
Step out of bicycle.
Put on stand.

## Slide 15: Hierarchy of Functions – Electric Bicycle Type D operation (Single person, long distance)
F0 – To travel on two wheels (Single person, long distance)
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security

## Slide 16: FFBD Type D (Single person long distance)
Electric bicycle (Level 0 Function)
Person at starting location
Arrive destination
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
System control activated
Driver ready to activate system
Control battery power
Control manual power
System auto-power
System manual-power
System speed
F6 – Armed seat

## Slide 17: Concept of Operations Type E (Goods, long distance)
Put armed seat with seat belt (to enhance seating).
Put goods carrier at back of bicycle.
Put helmet on.
Release the stand. Hands to hold the handles.
Sit on the bicycle. Feet on ground to support bicycle.
Insert key to bicycle. Turn power on.
Turn right handle forward to increase speed, allow right handle to relax to continue without adding power.
System limits max. speed 20 kmph (urban limit)
If more power is required, activate power surge function, then cycle paddle to assist.
Turn steering column to turn direction.
To stop, turn right handle backward to activate regenerative brake.
Wait to stop then put feet on ground to support bicycle.
Turn power off.
Step out of bicycle.
Put on stand.
Unload goods from goods carrier.

## Slide 18: Hierarchy of Functions – Electric Bicycle Type E operation (Goods, long distance)
F0 – To travel on two wheels (Goods, long distance)
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security

## Slide 19: FFBD Type E (Goods, long distance)
Electric bicycle (Level 0 Function)
Person at starting location
Arrive destination
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
System control activated
Driver ready to activate system
Control battery power
Control manual power
System auto-power
System manual-power
System speed
F6 – Armed seat

## Slide 20: Hierarchy of Functions – Electric Bicycle
F0 – Electric bicycle system
F1.1 – Steel frame
F1.2 – Pedal and chain
F1.3 – Wheels
F7.1 – RF activation
F7.2 – Passcode activation
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security

## Slide 21: F1 – Heavy duty bicycle FFBD
Heavy duty bicycle (Level 1 Function)
Person at starting location
Speed
F1.1 – Steel frame
F1.2 – Pedal and chain
F1.3 – Wheels
System manual-power
?
Pedal power
Rider sit on bicycle
System auto-power
F1.4 – Motor
AND
Motor power
Distance travelled (Rider arrive destination)

## Slide 22: Hierarchy of Functions – Electric Bicycle (amended due to F1)
F0 – Electric bicycle system
F1.1 – Steel frame
F1.2 – Pedal and chain
F1.3 – Wheels
F7.1 – RF activation
F7.2 – Passcode activation
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F5 – Goods carrier
F6 – Armed seat
F7 – System security
F1.3 – Wheels

## Slide 23: Concept of Operations – Rider authentication
Rider carries RF key near bicycle
System signals rider to use keypad to enter passcode
Rider keys passcode sequence to keypad
System signals authenticated. System is activated.
If System signals not authenticated. System keypad is locked.

## Slide 24: FFBD System security – rider authentication
F1 – Heavy duty bicycle
F2 – Bicycle system control
F3 – Battery
F4 – Manual assist
F7 – System security
System control activated
Rider approaches system with RF key
F6 – Armed seat
F5 – Goods carrier
Activation authorised
Electric bicycle (Level 0 Function)

## Slide 25: F7 – System security FFBD
System security (Level 1 Function)
Driver ready to activate system
Activation not authorised
F7.1 – RF activation
F7.2 – Passcode activation
Activation authorised
Request activation

## Slide 26: Questions?